## Slide 1: Middle Avenue and El Camino Real signal and conceptual geometric improvements
December 11, 2024

## Slide 2: AGENDA
Background
Evaluation
Feedback
Next Steps
Middle Ave. and ECR (view from eastbound Middle Ave.)

## Slide 3: Background (Permanent Improvements)
Mar. 2021: Middle Avenue complete streets project
Oct. 2022: traffic calming measures approved
May 2024: permanent buffered bike lanes approved

## Slide 4: Background (Pilot Projects)
Jan. 2024: Blake St. closure (no access to/from Middle Ave.)
Nov. 2024: Nealon Park frontage parking (back-in angle parking)
Nealon Park frontage parking
(back-in angle parking)
Blake St. closure (no access to/from Middle Ave.)

## Slide 5: Intersection evaluation (signal Operation)
Remove conflict b/t left turning vehicles from Middle Ave. onto ECR and oncoming traffic/ pedestrians/ bicyclists crossing ECR
Implement no right turn on red (RTOR) from Middle Avenue

## Slide 6: Intersection evaluation (signal Operation)
Alternatives | Lane configuration1 | Signal phasing2
Existing | LT + R | Permissive
Alt 1 – Existing with no RTOR | LT + R | Permissive
Alt 2 – Protected left with no RTOR | L + TR | Protected
Alt 2A – Protected left with RTOR | L + TR | Protected
Alt 3 – Dedicated bike signal phase | L + TR | Protected
Notes: RTOR = right turn on red LT = shared left & through lane, L = left turn only lane, TR = shared through & right lane, R = right turn only lane. Permissive = left turning vehicles yield to oncoming traffic and crossing pedestrian/bicyclists. Protected = left turning vehicles have no conflict. |  | 
Existing
Alternatives

## Slide 7: Intersection evaluation (signal Operation)
Alternatives | Lane configuration1 | Signal phasing2 | Key takeaway (compared to existing conditions)
Existing | LT + R | Permissive | Con: left turning vehicles from Middle Ave. conflict with oncoming traffic/ pedestrians/ bicyclists crossing ECR.
Alt 1 – Existing with no RTOR | LT + R | Permissive | Pro: most likely to be approved by Caltrans due to minimal impact to ECR. Con: left turning vehicles from Middle Ave. conflict with oncoming traffic/ pedestrians/ bicyclists crossing ECR. Con: right turn queue on Middle Ave. will worsen.
Alt 2 – Protected left with no RTOR | L + TR | Protected | Pro: resolve left turning vehicles from Middle Ave. conflict with oncoming traffic/ pedestrians/ bicyclists crossing ECR. Con: right turn queue on Middle Ave. will worsen. Con: ECR queue will worsen due to reduced green time.
Alt 2A – Protected left with RTOR | L + TR | Protected | Pro: resolve left turning vehicles from Middle Ave. conflict with oncoming traffic/ pedestrians/ bicyclists crossing ECR. Con: ECR queue will worsen due to reduced green time.
Alt 3 – Dedicated bike signal phase with no RTOR | L + TR | Protected | Pro: resolve left turning vehicles from Middle Ave. conflict with oncoming traffic/ pedestrians/ bicyclists crossing ECR. Pro: dedicated bike phase crossing El Camino Real Con: require more signal time and impact signal coordination. Con: least likely to be approved by Caltrans due to significant impact to ECR. Con: right turn queue on Middle Ave. will worsen.
Notes: RTOR = right turn on red LT = shared left & through lane, L = left turn only lane, TR = shared through & right lane, R = right turn only lane. Permissive = left turning vehicles yield to oncoming traffic and crossing pedestrian/bicyclists. Protected = left turning vehicles have no conflict. |  |  | 

## Slide 8: Intersection evaluation (signal Operation)
Approach | Lane storage (ft) | Existing (ft) | Alt 1 – Ex. w/ no RTOR (ft) | Alt 2 – Prot. Left w/ no RTOR (ft) | Alt 2A – Prot. Left w/ RTOR (ft) | Alt 3 – Dedicated bike phase w/ no RTOR (ft)
Northbound Middle Ave. |  |  |  |  |  | 
NBL | 150 turn lane & 980 to Blake St. | 390 (420) | +1,110 (+310) | +880 (+180) | +330 (+0) | +1,110 (+0)
NBT |  |  |  | +30 (+90) | +50 (+20) | +0 (+50)
NBR |  | 340 (290) | +30 (+110) |  |  | 
Southbound Middle Ave. |  |  |  |  |  | 
SBL | 80 turn lane & 250 to garage entrance | 100 (190) | +0 (+0) | -20 (-80) | -30 (-60) | -20 (-70)
SBT |  |  |  | +60 (+110) | +40 (+90) | +50 (+95)
SBR |  | 40 (70) | +0 (+30) |  |  | 
Westbound ECR |  |  |  |  |  | 
WBL | 280 turn lane & 1070 to Cambridge Ave. | 260 (410) | +10 (+0) | +110 (+0) | +60 (+0) | +160 (+0)
WBT |  | 330 (710) | +0 (+100) | +80 (+500) | +0 (+530) | +600 (+660)
Eastbound ECR |  |  |  |  |  | 
EBL | 220 turn lane & 830 to Roble Ave. | 130 (170) | +30 (+10) | +120 (+10) | +90 (+0) | +70 (+0)
EBT |  | 450 (510) | +0 (+0) | +20 (+20) | +70 (+0) | +0 (+0)
Notes: ## (##) = morning (evening) commute hour Results represent the 95 percentile queue length. |  |  |  |  |  | 
Notes: Mention the approach orientation being different than SR.

## Slide 9: Intersection evaluation (signal Operation – morning commute hour 95% queue)
Notes: Mention the approach orientation being different than SR.

## Slide 10: Intersection evaluation (signal Operation – Evening commute hour 95% queue)
Notes: Mention the approach orientation being different than SR.

## Slide 11: Intersection evaluation (Geometry)
Improve pedestrian/bicycle conditions
ECR
Middle Ave.

## Slide 12: Intersection evaluation (Geometry)
Potential impacts (right of way, utility conflicts, budget & schedule)
ECR
Middle Ave.

## Slide 13: Feedback
Signal – which alternative for further analysis?
Geometry – is there consensus to continue or pause design due to constrains (utility relocation, ROW acquisition)?

## Slide 14: Next Steps
Incorporate CSC feedback
Present to City Council

## Slide 15: Thank you